## Slide 1
Module 7
I²C — Protocol + RTL + Basic Testbench
learn_uart_spi_i2c / Module 7

## Slide 2
Learning objectives
• How START/STOP are detected/produced (SDA
transitions while SCL high).
• How the address + R/W bit and data bytes are
serialized on SDA.
• How to build a basic “bus monitor” that reconstructs
bytes by sampling SDA on SCL rising edges.
learn_uart_spi_i2c / Module 7

## Slide 3
Prerequisites
• Modules 1–6.
• Verilator, Make, C++ compiler. No UVM required for
this baseline.
learn_uart_spi_i2c / Module 7

## Slide 4
Learning path
Understand the I²C protocol (start/stop, addressing, ACK/NACK), translate it to RTL (simple master + timing), and verify with a **basic** (…
learn_uart_spi_i2c / Module 7

## Slide 5
Overview
• Module 7 is the I²C **protocol + RTL + basic
testbench** module (UVM comes in Module 8).
learn_uart_spi_i2c / Module 7

## Slide 6
Syllabus topics
learn_uart_spi_i2c / Module 7

## Slide 7
1. I²C Protocol Essentials
• Bus idle: SCL=1, SDA=1.
• START: SDA goes 1→0 while SCL is 1.
• STOP: SDA goes 0→1 while SCL is 1.
• Address phase: 7-bit address + R/W bit (0=write,
1=read) sent MSB first.
• Data phase: 8-bit data bytes sent MSB first.
• ACK/NACK (concept): receiver pulls SDA low for ACK
on the 9th clock; high means NACK.
learn_uart_spi_i2c / Module 7
Notes: From MODULE7 Topics Covered.

## Slide 8
2. RTL Architecture (Baseline)
• clk_div: Divides `clk` to produce `clk_div_tick`
used to toggle/advance SCL timing.
• i2c_master: State machine that generates:
• START condition
• address+W bits
• one data byte
• STOP condition
learn_uart_spi_i2c / Module 7
Notes: From MODULE7 Topics Covered.

## Slide 9
3. Basic Testbench
• Stimulus: Pulses `start`, sets `addr` and `data_in`,
waits for `done`.
• Monitor/self-check: Detects START, then samples SDA
on each rising edge of SCL to reconstruct:
• 8 bits of address+W
• 8 bits of data
learn_uart_spi_i2c / Module 7
Notes: From MODULE7 Topics Covered.

## Slide 10
Hands-on examples
learn_uart_spi_i2c / Module 7

## Slide 11
Module 7 self-check
$ ./scripts/module7.sh --check
learn_uart_spi_i2c / Module 7
Notes: Run from course repository root.

## Slide 12
Example 1: I²C baseline
• Drives a single write transaction (START → address+W
→ data → STOP)
• Includes a simple bus monitor that samples SDA on
SCL rising edges to reconstruct bytes
• No UVM
learn_uart_spi_i2c / Module 7
Notes: module7/examples/i2c_baseline/README.md

## Slide 13
Demo: I²C baseline
$ ./scripts/module7.sh --run
learn_uart_spi_i2c / Module 7
Notes: Hands-on: module7/examples/i2c_baseline/

## Slide 14
Practice & assessment
learn_uart_spi_i2c / Module 7

## Slide 15
Exercises
• Run i2c_baseline
• Trace one transfer
• Bus monitor
• Optional: Waveforms
learn_uart_spi_i2c / Module 7

## Slide 16
Assessment checklist
• Can describe I²C START, STOP, address+R/W, and data
phase (and ACK/NACK concept).
• Can explain the role of i2c_master and clk_div; know
the baseline uses push-pull (simplified).
• Can run i2c_baseline and interpret the test result.
• Ready for Module 8: I²C UVM+SV verification.
learn_uart_spi_i2c / Module 7

## Slide 17
Summary & next steps
• Understand the I²C protocol (start/stop, addressing,
ACK/NACK), translate it to RTL (simple master…
• Complete module7/CHECKLIST.md
• Run ./scripts/module7.sh --check
• Next: I²C UVM+SV
learn_uart_spi_i2c / Module 7