## Slide 1
Module 8
I²C — UVM+SV Verification
learn_uart_spi_i2c / Module 8

## Slide 2
Learning objectives
• I²C UVM agent: I2cTransaction, I2cSequence,
I2cDriver, I2cMonitor, I2cScoreboard.
• Interface: i2c_if (clk, rst_n, start, addr, data_in,
scl, sda, clk_div_tick, busy, done) connects U…
• How to hook up a UVM monitor and scoreboard to a
bus-oriented DUT.
learn_uart_spi_i2c / Module 8

## Slide 3
Prerequisites
• Module 7 (I²C protocol + RTL + basic TB).
• Verilator, Make, C++ compiler, UVM (UVM_HOME or
vendored UVM).
learn_uart_spi_i2c / Module 8

## Slide 4
Learning path
Extend I²C verification to **UVM+SV** — I²C agent (transaction, sequence, driver, monitor, scoreboard); run on Verilator.
learn_uart_spi_i2c / Module 8

## Slide 5
Overview
• Module 8 builds on Module 7 (I²C protocol + RTL +
basic testbench):
learn_uart_spi_i2c / Module 8

## Slide 6
Syllabus topics
learn_uart_spi_i2c / Module 8

## Slide 7
1. I²C UVM Agent
• Transaction (I2cTransaction): address and data to
write; monitor fills observed_addr/observed_data.
• Sequence (I2cSequence): produces directed
transactions (e.g. same addr, different data bytes).
• Driver (I2cDriver): gets transaction, drives
start/addr/data_in for one cycle, waits for done.
• Monitor (I2cMonitor): watches SCL/SDA; after START,
samples SDA on rising SCL to reconstruct 8 bits…
• Scoreboard (I2cScoreboard): compares expected (from
test) vs observed_addr/observed_data.
learn_uart_spi_i2c / Module 8
Notes: From MODULE8 Topics Covered.

## Slide 8
2. Toolchain
• Same as Module 6 (SPI UVM): Verilator with -sv,
--timing, --trace, UVM include paths, `make SIM=ver…
learn_uart_spi_i2c / Module 8
Notes: From MODULE8 Topics Covered.

## Slide 9
Hands-on examples
learn_uart_spi_i2c / Module 8

## Slide 10
Module 8 self-check
$ ./scripts/module8.sh --check
learn_uart_spi_i2c / Module 8
Notes: Run from course repository root.

## Slide 11
Example 1: I²C UVM
• UVM phases and reporting (DRIVER, MONITOR,
SCOREBOARD).
• Scoreboard checks (expected vs observed address+data
from the bus).
• Final scoreboard summary (matches and mismatches).
learn_uart_spi_i2c / Module 8
Notes: module8/examples/i2c_uvm/README.md

## Slide 12
Demo: I²C UVM
$ ./scripts/module8.sh --run
learn_uart_spi_i2c / Module 8
Notes: Hands-on: module8/examples/i2c_uvm/

## Slide 13
Practice & assessment
learn_uart_spi_i2c / Module 8

## Slide 14
Exercises
• Run i2c_uvm
• Trace one transaction
• Change the sequence
• Compare across protocols
learn_uart_spi_i2c / Module 8

## Slide 15
Assessment checklist
• Can describe the I²C UVM agent and how it maps to
I²C (addr+data, monitor on SCL/SDA).
• Can run i2c_uvm and interpret UVM output.
• Can compare UVM structure across UART, SPI, and I²C.
learn_uart_spi_i2c / Module 8

## Slide 16
Summary & next steps
• Extend I²C verification to **UVM+SV** — I²C agent
(transaction, sequence, driver, monitor, scoreboa…
• Complete module8/CHECKLIST.md
• Run ./scripts/module8.sh --check
• Next: Next module in course
learn_uart_spi_i2c / Module 8